## Slide 1: Stress-Aware Driving App
Spotting driver distress from a heart signal, and stopping safely. AI product overview, October 2026.
Affreen Jha
Notes: About 20 seconds. Good morning. This is the Stress-Aware Driving App: a prototype that watches a driver's heart signal, spots sustained distress, and responds in stages, from a warning to a simulated pull-over onto the shoulder. I'll cover why it matters, how it works, what is built, what it costs, and what comes next, in about five minutes.

## Slide 2: A rare event with severe outcomes
683,491
US heart disease deaths in 2024, the leading cause
1.3%
of drivers in surveyed US crashes were in a medical emergency
39,254
US traffic deaths in 2024
In one 30-case autopsy series, most drivers who suffered cardiac arrest at the wheel stopped the vehicle without injury. There is often a short window to act.
Sources: CDC; NHTSA; Antecol and Roberts (1990)
Notes: About 25 seconds. Heart disease is the leading cause of US deaths. Medical emergencies behind the wheel are a small share of crashes, about 1.3 percent of drivers in one NHTSA survey, but those crashes are more often severe. Drivers who have an event often have a short window to act. That window is the gap this product targets.

## Slide 3: From wrist to a safe stop
Sensor
Reads pulse and beat intervals
Car app
Decodes and checks the data
AI score
Scores distress from 0 to 100
Agent
Acts only if distress persists
Safe stop
Slows, merges right, stops
All vehicle control is simulated. Slate steps sense and process; red steps act.
Notes: About 30 seconds. Here is the path. A sensor reads pulse and beat intervals. The car app decodes it and checks it is plausible. The AI layer scores distress from zero to one hundred. The agent only acts if distress persists. If it does, the simulated car slows, merges right, and stops on the shoulder. All vehicle control is simulated.

## Slide 4: Two signals become one distress score
Heart rate above baseline
up to 60 points
Full score at 30 bpm over your resting rate
Low heart-rate variability
up to 40 points
RMSSD at or below 15 ms scores the full 40
Distress score, 0 to 100
Normal
Distress
Severe
0
60
80
100
60 or more starts the timers
80 or more for 20 s escalates
Baseline learned in the first 15 s
Starting defaults, not clinical thresholds
Notes: About 30 seconds. The score combines two signals. Heart rate above your resting baseline can add up to sixty points, and low heart-rate variability can add up to forty. A score of sixty starts the timers; eighty or more for twenty seconds escalates. These are starting defaults, not clinical thresholds.

## Slide 5: The agent escalates one step at a time
Normal
SCORE
Under 60
CAR
Lane 1, 70 mph
SCREEN
Green gauge
Watch
SCORE
Over 60, under 5 s
CAR
No change
SCREEN
Amber badge
Intervene
SCORE
Over 60 for 5 s
CAR
Slows, merges right
SCREEN
Red banner
Escalate
SCORE
80+ for 20 s
CAR
Stops on shoulder
SCREEN
15 s countdown
A score below 60 returns the agent to normal from any state.
Notes: About 30 seconds. The agent climbs a ladder. Normal: lane one at seventy miles an hour. Watch: distress for under five seconds, we only observe. Intervene: five seconds sustained, the car slows and merges right. Escalate: eighty or more for twenty seconds, it stops on the shoulder and starts a fifteen second countdown.

## Slide 6: A human stays in control
Cancel any time
15 second countdown with an I'm OK button
Never calls 911
Silence alerts a personal contact. Call 911 stays a manual tap
Data guardrails
Rejects impossible readings, flags stale data, limits speed changes
Simulation only
No link to a real vehicle
Notes: About 30 seconds. Safety is built in. The driver can cancel any escalation. If they do not respond, a personal contact is notified, never 911, and a manual call button is always on screen. Guardrails reject impossible readings and limit how fast speed can change. And all vehicle control stays in a simulator.

## Slide 7: The prototype is largely built
Chart: 20 requirements: built vs next
| Built | Next
Requirements | 16 | 4
6 of 6
scenario evals passing
Bluetooth heart-rate intake
Guardrails and event log
AI scoring and escalation agent
Freeway simulator dashboard
Next: dead-man's alert, watch relay, retries, confidence gate
Notes: About 25 seconds. Sixteen of twenty requirements are built, and all six scenario evals pass. Next up are four items: the dead-man's alert for sensor loss, watch relay support, notification retries, and a confidence gate before any intervention.

## Slide 8: Heart rate flags distress, not disease
Heart rate and HRV cannot separate stress from a cardiac event
So the app flags distress and never diagnoses.
Wrist data is noisy
Motion and skin tone distort readings
Silent sensor loss
A dead battery can look like a calm driver
Simulation only
Real vehicle control needs ISO 26262 validation
Notes: About 30 seconds. Be clear about the limits. Heart rate and variability cannot separate stress from a cardiac event, so this flags distress and never diagnoses. Wrist sensors are noisy, a dead battery can look like a calm driver, and real vehicle control would need functional-safety validation. Those limits shape our roadmap.

## Slide 9: Hardening comes before new features
0
Prototype
Intake and scoring
Agent, guardrails
Evals, simulator
1
Harden
Dead-man's alert
Confidence gate
Noise filter
Notification retries
2
Validate
Replay evals
Skin tone, motion
Watch relay
3
Extend
Camera check
Learned model
Driver baselines
Gate 1
P0 built, evals green
Gate 2
Targets met on data
No real-vehicle use without functional-safety validation (ISO 26262) and regulatory approval.
Notes: About 30 seconds. The roadmap has four phases. Prototype is done. Harden is next: the dead-man's alert, a confidence gate, a noise filter, and notification retries. Then validate on recorded data, including skin tone and motion. Two gates keep us honest: first, core requirements built and evals green; then, targets met on recorded data.

## Slide 10: Finishing the roadmap: about $91K
Chart: One-time cost by scenario
| Lean | Base | Full
One-time cost ($K) | 51.7 | 90.6 | 142.3
95%
of the base build is people time
$8.9K
a year to run (Base)
<$4K
hardware, SMS and tools (Base)
Hours and rates are assumptions; prices from retailer and Twilio pages.
Notes: About 30 seconds. Finishing phases one to three costs about ninety-one thousand dollars in the base case, from about fifty-two thousand lean to one hundred forty-two thousand with external validation. Ninety-five percent is people time, so hours and rates matter far more than hardware. Running it costs about nine thousand dollars a year. These are assumptions to replace with your own quotes.

## Slide 11: North Star: safe-response rate
How often the car starts slowing within 6 seconds of sustained distress, with zero false interventions on calm sessions.
Three decisions now
1
Choose the first supported watch
2
Build the dead-man's alert (FR-7)
3
Collect recorded sessions for replay evals
Thank you. Questions welcome.
Notes: About 30 seconds. Our North Star is the safe-response rate: how often the car starts slowing within six seconds of sustained distress, with zero false interventions on calm sessions. Three decisions for now: pick the first supported watch, build the dead-man's alert, and start collecting recorded sessions. Thank you, and questions are welcome.